## Slide 1
Life Cycle Engineering Application
PLA vs. Biodegradable PPE Food Packaging Containers
Course: Life Cycle Engineering 2026
Professor: Paulo Peças
Group Members: ____________________
Date: July 1, 2026
Why this product?
Takeaway containers are high-volume single-use items and a major lever for plastic-waste reduction under EU policy shifts.

## Slide 2
Product Characterization, Alternatives, and Process Model
• Functional Unit: 1,000 containers (500–750 mL)
• Market Size (EU): 8–10 billion units/year
• Requirements: food-safe, heat-resistant, lightweight, low-cost, scalable
• PLA: density 1.24 g/cm³ | thermoforming | ~55°C | industrial composting
• PPE: density 0.90 g/cm³ | injection moulding | up to 100°C | limited compostability
PLA Process Chain
PLA granulate
Sheet extrusion
Thermoforming
Trimming
Packaging
PPE Process Chain
PPE granulate
Injection moulding
Cooling
Ejection
Packaging
• Machine Selection: PLA → Thermoforming machine | PPE → Injection moulding machine

## Slide 3
Core Results: LCC and LCA (per 1,000 containers)
• LCC Total: PLA = €66.3 | PPE = €54.4 → PPE economically superior
• Material: 39.6 vs 22.4 | Energy: 6.5 vs 8.2
• Labour: 12 vs 12 | Depreciation: 4 vs 6 | Tooling: 3 vs 5 | Waste: 1.2 vs 0.8
LCC Total Cost Comparison
PLA
66.3
PPE
54.4
• LCA Highlights
• GWP (kg CO₂-eq): PLA 28 vs PPE 34 (PLA better)
• Energy Demand (MJ): PLA 420 vs PPE 510 (PLA better)
• Water Use (L): PLA 180 vs PPE 60 (PPE better)
• End-of-life performance depends on composting availability for PLA.
GWP
Energy
Water
Green=PLA Orange=PPE

## Slide 4
Sensitivity, Positioning, and Final Recommendation
Sensitivity Analysis (Professor Required)
• PLA is highly sensitive to feedstock/material price (±20%).
• PPE is highly sensitive to energy price (±30%).
• Higher scrap rates penalize PLA more strongly.
• PLA outcome depends on composting infrastructure quality.
• PPE gains from large-scale production volumes.
Sensitivity Tornado (relative impact)
Material price
Energy price
End-of-life
Scrap rate
Volume
Alternatives Mapping (Cost–Environment–Technical)
Environment
Cost
Technical
PLA
PPE
Final conclusions:
• PLA: best environmental option (if composting is available).
• PPE: best economic + technical option (especially hot food).
• Recommended for deployment: choose by temperature, waste system, and budget.

## Slide 5
MANUFACTURING PROCESS – TAKEAWAY FOOD CONTAINER (650 mL)
PROCESS 1: PLA – THERMOFORMING
1
PLA GRANULATE
PLA resin pellets used as raw material.
Image placeholder
2
SHEET EXTRUSION
PLA granulate is melted and extruded into continuous sheets.
Image placeholder
3
THERMOFORMING
Heated PLA sheet is formed into container shape using vacuum forming.
Image placeholder
4
TRIMMING
Excess material (flange) is trimmed to final container shape.
Image placeholder
5
PACKAGING
Containers are stacked and packed for distribution.
Image placeholder
FINAL PRODUCT (PLA)
• Material: PLA (Thermoformed) • Capacity: 650 mL • Color: Natural / Beige • Lightweight & compostable • Suitable up to ~55°C
PROCESS 2: BIODEGRADABLE PPE – INJECTION MOULDING
1
PPE GRANULATE
Biodegradable PPE pellets used as raw material.
Image placeholder
2
INJECTION MOULDING
Pellets are melted and injected into mould cavity under pressure.
Image placeholder
3
COOLING
Mould is cooled to solidify the container shape.
Image placeholder
4
EJECTION
Container is ejected from the mould.
Image placeholder
5
PACKAGING
Containers are inspected, stacked and packed for distribution.
Image placeholder
FINAL PRODUCT (PPE)
• Material: Biodegradable PPE • Capacity: 650 mL • Color: Natural / White • Heat resistance up to 100°C • Durable & food safe
PROCESS COMPARISON SUMMARY
TECHNOLOGY PLA: Thermoforming PPE: Injection Moulding
CYCLE TIME (APPROX.) PLA: 6–8 sec PPE: 4–6 sec
SCRAP RATE PLA: ~12% PPE: ~4%
HEAT RESISTANCE PLA: ~55°C PPE: up to 100°C
END-OF-LIFE PLA: Industrial compostable PPE: Limited compostability
APPLICATION Both suitable for takeaway food packaging

## Slide 6
COST & ENVIRONMENTAL COMPARISON CHARTS (PLA vs BIODEGRADABLE PPE)
Chart: LCC Breakdown per 1,000 Containers
| Material | Energy | Labour | Machine Dep. | Tooling | Waste | Total LCC
PLA (€) | 39.6 | 6.5 | 12 | 4 | 3 | 1.2 | 66.3
PPE (€) | 22.4 | 8.2 | 12 | 6 | 5 | 0.8 | 54.4
Chart: LCA Impact Comparison
| GWP (kg CO2-eq) | Energy Demand (MJ) | Water Use (L)
PLA | 28 | 420 | 180
PPE | 34 | 510 | 60
Sensitivity Snapshot (Editable Diagram)
Material price (±20%)
PLA more sensitive
Energy price (±30%)
PPE more sensitive
Scrap rate
PLA penalty higher
End-of-life scenario
PLA depends on composting
Production volume
PPE gains at scale
Key Takeaways • PPE is economically superior (Total LCC: €54.4 vs €66.3). • PLA performs better in GWP and energy demand. • PPE performs better in water use and heat resistance. • Final choice depends on temperature requirements, composting infrastructure, and cost constraints.